## Slide 1: Understanding Data Part 1
Representing Data Digitally

## Slide 2: Data
Data values can be stored in variables, lists of items, or standalone constants.
Computing devices represent data(text, numbers, audio, images) digitally, meaning that the lowest-level components of any value are bits.
Bit is shorthand for binary digit and is either 0 or a 1. This system of representing data is called binary (base 2) which uses only combinations of the digits zero and one.
name = "Mike Smith" # represented internally as 0's and 1's
grades = [87, 91, 75] # represented internally as 0's and 1's
Thus, digital data is simply some sequence of 0's and 1s representing some information.

## Slide 3: Base 10 (Decimal numbers)
Computers store all information in the form of binary numbers. To understand binary numbers, let's first look at a more familiar system: decimal numbers.
Decimal numbers is base 10. It uses 10 digits {0,1,2,3…,9}. Why do we prefer base 10? There are many reasons but one simple reason is simply because we have ten fingers.
Base 10 (Decimal) uses 10 digits: {0,1,2,3…,9}.
Base 2 (Binary) uses 2 digits: {0,1}.
Base 8 (Octal) uses 8 digits: {0,1,2,3,4,5,6,7}
Base 16 (Hexadecimal) uses 16 digits: {0,1,2,3,4…,9,A,B,C,D,E,F}

## Slide 4: Base 10 (Decimal numbers)
Each digit has a weight corresponding to a power of 10. Multiply each digit with its weight and then sum.
What does 157 mean?
  157 = 1 x 100 + 5 x 10 + 7 x 1
= 1 x 102 + 5 x 101 + 7 x 100

## Slide 5: Base 10 (Decimal)

## Slide 6: Base 2 (Binary)

## Slide 7: Base 2 (Binary)
Base 2
1011 = 1 x 23 + 0 x 22 + 1 x 21 + 1 x 20
1011 = 1 x 8 + 0 x 4 + 1 x 2 + 1 x 1 =11 in Base 10

## Slide 8: Bits and Bytes
1 bit is a single bit of information, a 1 or 0(Only two possible values)
1 byte is 8 bits, an 8-bit word
  256 possible values from 0-255 base 10
  or 00000000 to 11111111 base 2
For example, 10100110 is a single byte.

## Slide 9: Decimal to Binary
Repeatedly modulo 2 and the divide by 2. Stop at 0. The remainder list read top to bottom are the digits from left to right.

## Slide 10: People
There are 10 types of people in the world; those who understand binary and those who don’t.
There are 10 types of people in the world; those who understand binary and those who have friends.

## Slide 11: Hexadecimal
Binary code is too long in representation. Hexadecimal is much shorter. Hexadecimal uses 16 digits.
Problem: we are short of numbers.
  A-10 B-11 C-12 D-13 E-14 F-15
  Hexadecimal digits: {0,1,2,3,4…,9,A,B,C,D,E,F}
Converting a binary number to a Hex number is relatively easy. Every 4 bits can convert to a Hex.

## Slide 12: Hexadecimal

## Slide 13: Binary to Hex

## Slide 14: Counting
Let’s count in Base 10.
0,1,2,3,4,5,6,7,8,9,__,___,…,18,19,__,__.
Answer: 10,11…..,20,21. Good job!
Let’s count in Base 5.
0,1,2,3,4,__,__,__,__,__,___.
Answer:10,11,12,13,14,20.
Let’s keep going!
40,41,42,43,44,___,___,___.
Answer:100,101,102.

## Slide 15: Quick Quiz
What’s the answer in base 8?
What’s the answer in base 5?
What’s the answer in base 12?

## Slide 16: Overflow Error
﻿
In many programming languages, integers are represented by a fixed number of bits, which limit the range of integer values and mathematical operations on those values.
For example in Java, the range of the value of an integer is from −2,147,483,648 to +2,147,483,647. Trying to store a number bigger than the limits will result in an overflow error.
Some languages like Python, integers do not have limits on number size but, instead, expand to the limit of the available memory.

## Slide 17: Overflow Error
The formula to calculate the largest number stored using n bits is 2^n – 1.
Example 1:
With 4 bits, the largest integer that can be stored is 2^4 - 1 = 15.
Example 2:
A 4-bit integer can any value in {0,1,2,..,15}. Thus, storing the value of 10 + 6 = 16 would cause an overflow error since the 16 = 10000 requires at least 5 bits.
Example 3:
If x is a 3-bit integer, then x = 111 + 111 will cause an overflow error since the sum is 1110 which requires at least 4 bits.

## Slide 18: Round Off Errors
A fixed number of bits is used to store real numbers. Because of this limitation, round-off errors can occur.
Python computes 1/3 as 0.3333333333333333. This value is only an approximation of 1/3 which is an infinitely repeating decimal.
Round-off error occurs when decimals (real numbers) are rounded.

## Slide 19: Abstraction
Abstraction is the process of reducing complexity by focusing on the main idea.
By hiding details irrelevant to the question at hand and bringing together related and useful details, abstraction reduces complexity and allows one to focus on the idea.
One type of abstraction we saw was procedural abstraction, which provides a name for a procedure(function) and allows it to be used only knowing what it does, not how it does it.
import random
print(random.randrange(10)) # random number from 0 - 9
We don't need to know how the randrange() function is implemented to be able use it.

## Slide 20: Abstraction
Bits are grouped to represent abstractions. These abstractions include, but are not limited to, numbers, characters, and color.
Sequences of 0's and 1's represent a string of characters, a numeric grade and a color in the examples below. The color example is done using Processing.
name = "Mike Smith"
grade = 87
c = color(255, 123, 110)
fill(c);
ellipse(250, 80, 100, 100)

## Slide 21: Encoding
A computer cannot store “letters” or “pictures”. It can only work with bits(0 or 1).
To represent anything other than bits, we need rules that will allow us to convert a sequence of bits into letters or pictures. This set of rules is called an encoding scheme, or encoding for short. For example,

## Slide 22: ASCII
ASCII(American Standard Code for Information Exchange) is an encoding scheme that specifies the mapping between bits and characters. There are 128 characters in the scheme. There are 95 readable characters and 33 values for nonprintable characters like space, tab, and backspace and so on.
The readable characters include a-z, A-Z, 0-9 and punctuation. In ASCII, 65 represents A, 66 represents B and so on. The numbers are called code points. But ASCII only uses 8 bits. It does not have enough bits to encode other characters and languages(Chinese, French, Japanese).
Similar to ASCII, Unicode provides a table of code points for characters: "65 stands for A, 66 stands for B and 9,731 stands for ☃”. UTF-32(Unicode Transformation Format), UTF-16 and UTF-8 are three encodings that use the Unicode table of code points.
Of the three, UTF-8 is by far the most widely used encoding. It is the standard encoding for all email and webpages(HTML5).

## Slide 23: ASCII Sample
To encode something in ASCII,
follow the table from right to left,
substituting letters for bits.
To decode a string of bits into
human readable characters, follow
the table from left to right, substituting
bits for letters.
decode
encode

## Slide 24: Sequences of Bits
What does a list of numbers, an image and an audio file have in common?
They are all just lists of numbers!
The same sequence of bits may represent different types of data in different contexts.
import numpy as np
import matplotlib.pyplot as plt
nums = np.loadtxt("numbers.txt")
print(nums) # array([210 190 225 ..., ])
print(nums.size) # 783126
These numbers can represent anything. For example, it could represent the number of characters in a list of 783,126 tweets that were tweeted over some one-minute interval.
Or this same list could represent something else entirely. See the next slide!
img = plt.imread("flower.jpg")
print(img.shape) # (859, 840, 3)
fig, ax = plt.subplots()
ax.imshow(img)
imshow() displays the 2D
grid of pixels as an image.

## Slide 25: List of Numbers is An Image
The list of numbers in the previous example is now an image! We'll discuss how to write the code below in the next lecture.
import numpy as np
import matplotlib.pyplot as plt
nums = np.loadtxt("numbers.txt", dtype="uint8")
print(nums) # array([210 190 225 ..., ]), same list of numbers
nums = nums.reshape(417, 626, 3)
fig, ax = plt.subplots()
ax.imshow(nums)
The following output is
produced by running the above
code on the Jupyter Notebook

## Slide 26: Digital vs. Analog
Computers can only understand digital data: discrete values like a list of integers, sequences of 0's and 1's.
Analog data have values that change smoothly, rather than in discrete intervals, over time. Some examples of analog data include temperatures over a period of time, pitch and volume of music, colors of a painting, or position of a sprinter during a race.
  analog signals are continuous and can take on an infinite possible values(the real numbers)
  digital signals are finite. For example, 8-bit colors can take on one of 256 discrete, finite possibilities. But actual colors can take on any of an infinite possible values or shades.
Notes: Crash Course: Cybersecurity

## Slide 27: Digital vs. Analog
Analog data can be closely approximated digitally using a sampling technique, which means measuring values of the analog signal at regular intervals called samples.
The samples are measured to figure out the exact bits required to store each sample. The number of samples measured per second is the sampling rate, the higher the rate the better the quality.
CD-quality has a rate of 44,100 samples
per second(44,100 Hz or 44.1 kHz).
Analog Low sampling rate High sampling rate
Notes: Crash Course: Cybersecurity